## Slide 1: Multilevel Wavelet Packet Entropy
A New Strategy for Lung Sound Feature Extraction Based on Wavelet Entropy
Achmad Rizal, Risanuri Hidayat, Hanung Adi Nugroho
Department of Electrical Engineering and Information Technology, Universitas Gadjah
School of Electrical Engineering, Telkom University
rizal.s3te14@mail.ugm.ac.id

## Slide 2: Introduction
Biological signal  structural richness (Costa, 2005)
Lung sound  respiration process  complex system  complex signal (Kitaoka, 1999)
Some signal complexity metrics: Hjorth descriptor, fractal dimension, correlation dimension, entropy

## Slide 3: Introduction
Entropies: Shannon, Renyi, Tsallis, Spectral Entropy, Wavelet Entropy, Sample Entropy, Approximate entropy, Permutation entropy
Wavelet analysis + entropy = wavelet entropy / WE (Rosso, 2001)
Some WE extension : wavelet packet entropy (Safara, 2012)(Chen, 2015)

## Slide 4: Introduction
Some WPE variations:
WPD + Perm entropy (Yan, 2009)
WPE (using Shannon, TE and RE) (Li&Zhou 2016)
Wavelet time entropy (2014)
Proposed method:
Multilevel wavelet packet entropy

## Slide 5: Wavelet Entropy
E1 = energy of D1
E2 = energy of D2
E3 = energy of D3
E4 = energy of A3
Etot = ∑Ei i = 1,…,4

## Slide 6: Wavelet Packet Entropy

## Slide 7: Material & Method

## Slide 8: Material and Method
Format *.wav, fs= 8000Hz, 1 respiration cycle
http://jan.ucc.nau.edu/~daa/heartlung/breathsounds/contents.html.
http://www.rale.ca/Repository.htm.
http://www.med.ucla.edu/wilkes/lungintro.htm

## Slide 9: Material and Method
MWPE
Mother wavelet: Haar, Db2, Db8, Bior1.3, Bior2.8
Decomposition level: 1-7
Classifier : Multilayer Perceptron
Validation : three-fold cross validation

## Slide 10: Results and Discussion
stridor
Pleural rub

## Slide 11: Results and Discussion
WPE (70.71% Bior2.8, N = 1)

## Slide 12: Results and Discussion
MWPE (97.98 %. DB8, N = 4 - 7)

## Slide 13: Results and Discussion
MWPE  information of signal complexity in multiresolution domain
Higher level decomposition ≠ higher accuracy
For lung sound analysis  N = 4

## Slide 14: Conclusion
wavelet entropy (WE) DWT
wavelet packet entropy (WPD)  WPD
MWPE  WPD using N decomposition level
MWPE  higher accuracy than WPE
Next study  MWPE for other biological signal

## Slide 15: Selected references
[A. Kandaswamy, C. S. Kumar, R. P. Ramanathan, S. Jayaraman, and N. Malmurugan, “Neural classification of lung sounds using wavelet coefficients.,” Comput. Biol. Med., vol. 34, no. 6, pp. 523–37, Sep. 2004.
[A. Hashemi, H. Arabalibiek, and K. Agin, “Classification of Wheeze Sounds Using Wavelets and Neural Networks,” in International Conference on Biomedical Engineering and Technology (2011), 2011, vol. 11, pp. 127–131.
A. Rizal, R. Hidayat, and H. A. Nugroho, “Multiresolution Modified Grey Level Difference for Respiratory Sound Classification,” Adv. Sci. Lett., vol 23, no 5, pp 3972–3974, May 2017.
O. A. Rosso, S. Blanco, J. Yordanova, V. Kolev, A. Figliola, M. Schu, and E. Bas, “Wavelet entropy : a new tool for analysis of short duration brain electrical signals,” J. Neurosci. Methods, vol. 105, pp. 65–75, 2001.
F. Safara, S. Doraisamy, A. Azman, A. Jantan, and S. Ranga, “Wavelet packet entropy for heart murmurs classification,” Adv. Bioinformatics, vol. 2012, 2012.

## Slide 16: Multilevel Wavelet entropy
Single level WE
Chart: Decomposition Level
| N = 2 | N = 3 | N = 4 | N = 5 | N = 6 | N = 7
Haar | 62.62 | 56.56 | 62.62 | 48.48 | 55.5 | 46.46
Db2 | 64.64 | 67.68 | 57.5 | 39.4 | 53.5 | 47.47
Db8 | 50.5 | 59.6 | 72.73 | 44.44 | 61.61 | 50.51
Bior1.5 | 69.7 | 66.67 | 55.56 | 41.41 | 56.57 | 53.53
Bior2.8 | 68.69 | 67.68 | 60.61 | 60.61 | 61.61 | 40.4

## Slide 17: Multilevel Wavelet entropy
MWE
Chart: Decomposition Level
| N = 2 | N = 3 | N = 4 | N = 5 | N = 6 | N = 7
Haar | 62.63 | 80.81 | 91.92 | 91.92 | 91.92 | 92.93
Db2 | 67.68 | 82.83 | 82.83 | 91.92 | 90.91 | 91.92
Db8 | 50.51 | 80.81 | 89.9 | 91.92 | 91.92 | 91.92
Bior1.5 | 72.72 | 83.84 | 93.94 | 91.92 | 91.92 | 89.9
Bior2.8 | 69.7 | 85.8 | 91.92 | 92.9 | 94.9 | 90.91